P.O. Box 5205 Youngstown, Ohio  44514		         		Email: sales@skimtech.com

Phone: (330) 774-5044   Fax: (330) 757-7606		         	Website: www.skimtech.com

Providing Skimming Solutions For Industries Worldwide

Product Overview

Skimall™ CUSTOM Model AG25 “Mini David” Skimming System

The Model AG25 Oil Skimming System is designed to remove free-floating oils, grease and other material from the surface of water in indoor and outdoor applications where space is limited.  The compact design makes it ideal for oil/water equalization tanks and in-ground separators, outfall basins and hundreds of other applications.  The custom AG25 skimmer can be supplied with ¼ - ½HP special-duty motor (custom voltage, frequency, explosion proof, etc.) and customized mounts for unique installations.

How The Skimmer Works:

The Model AG25 Oil Skimmer uses a specially formulated ¼” diameter collector tube (TigerTube™) that is sized in length for the application and welded into a continuous loop.  The ¼” TigerTube™ collector tube floats on the surface of water and is driven in a continuous loop by the skimmer.  Oils, fats, and grease cling to the outside surface of the TigerTube™ and are drawn into the skimmer.  The material drawn into the skimmer is scraped off the TigerTube™ by abrasive resistant scrapers (Dureon™ scrapers) and flows into a sludge pan with 3.0” drain coupling.  The clean side of the TigerTube™ collector tube is then driven back to the surface of the water by the skimmer to remove more material.

Typical Removal Rates:

- Light Oils & Grease - 4 GPH

- Medium Oils & Grease - 9 GPH

- Heavy Oils & Grease - 20 GPH

The Custom Model AG25 Oil Skimming System Can Supplied Complete With:

* Safety guard with integral Dureon™ scrapers & pressure blocks.

* ¼ - ½ HP Motor - specify voltage, frequency and any other special duty requirements.

* Custom mounting system with universal coupling for ease of installation.

* Sludge pan with 3.0” drain coupling.

* Weight - 50 lbs. (approximate).

* Dimensions (Length x Width x Height) - 20” x 16” x 14” (approximate).